##### Engineering Specifications

| Product | : | Battery Charger for 1 to 2 8.4V Li-on Batteries |
| --- | --- | --- |
| Customer | : |  |
| Customer No. | : |  |
| Model No. | : | LBC1020 |
| Design No. | : |  |
| Date | : | Apr 18, 2009 |

###### Customer Approval

| Signature | Approval Date |
| --- | --- |

###### Approval (EQ-RL: )

| Revision | Prepared by | Reviewed by | Approved by |
| --- | --- | --- | --- |
| 1.0 |  |  |  |

Contents

|  |  | Page |
| --- | --- | --- |
| 0 | Revision History and Deviation | 2 |
| 1 | Product Features | 3 |
| 2 | Electrical Performance and Tests | 3 |
| 3 | Mechanical Tests and Requirements | 4 |
| 4 | Environmental Conditions | 4 |
| 5 | Product Inspections | 5 |
| 6 | Cautions | 5 |
| 7 | Charging Times | 5 |
| 8 | Mechanical Drawing | 6 |
| 9 | Nameplate | 6 |

0 Revision History and Deviation

0.1 Revision History

| Revision | Date | By | Description of Change |
| --- | --- | --- | --- |
| 1.0 | APR 18 2009 |  | New release |

0.2 Notice of Deviation

| Customer Request | Samples Deviation | Mass production |
| --- | --- | --- |
| Notice of items to be completed before mass production |
| Description | L/T | Remarks |

1 Product Features

1.1 Battery Type

Suitable for 1 to 2  8.4V  Li-on batteries.

1.2 Reverse Polarity Protection

The electrical circuit protects the charger and batteries from being damaged by  incorrectly installed batteries.

1.3 Low Battery Leakage Current

If the battery charger is not connected to input power and left in the charger, the charger will discharge the batteries using a pre-determined current.

2 Electrical Performance and Tests

2.1 Input Voltage

100~240V AC 50/60Hz  5W  MAX

2.2 Charging Voltage

Two (2) 8.4VDC channels

2.3 Charging Current

100mA ± 20mA

2.4  Charging Time Control.

2.5 Input Standby Current

Maximum 15mA

2.6 Input Loading Current

Maximum 100mA

2.7 Charging Indicators

Charging : the Red LED is on ,

Fully charged : the Green LED is on ,

2.8 Hi-pot Test

Apply 3000V AC between input plug and charging channel for 1 minute. Current leakage must be less than 5 mA.  After the test, the unit should still work as normal.

2.9 Insulation Resistance

Minimum 100M ohms @ DC500V

3 Mechanical Tests and Requirements

3.1 Drop test

Drop from a height of 3 feet onto a concrete floor covered with 1/8 inch vinyl tile.  Drop 3 times total, each time on a different product surface.

Expected result: The unit should meet section 1.7. requirements.

3.2 Surface

Damage and rusting are not permitted.

#### 4 Environmental Conditions

4.1 Operating Temperature

0℃ to 40℃, best at 25℃

4.2 Storage Temperature

-20℃ to 60℃, best at 25℃

4.3 Safety Standard

## 5 Product Inspections

5.1 Inspections of all products

- Charging voltages (2.2)

- Charging current (2.3)

- LED indicators (2.7)

- Hi-pot (2.8)

- Surface (3.2)

- Outside intense vibration

- Polarity of charging channel

5.2 Inspections of selected products

- Battery charging test

- Drop test (3.1)

## 6 Cautions

- Children should use product only under adult supervision.

- Mixing batteries of different capacities and sizes in the charger may influence the charging times or damage the batteries.

- Correctly insert the batteries and avoid reversing the +/- polarities.

- Cut off power after the batteries are fully charged.

- The charger is intended for use with Ni-MH/NiCd batteries only. Charging other battery types may cause explosions, breakage, personal injury or property damage.

- Incorrect use may result in electric shock

- For indoor use only. Keep away from humid and hot places.

- Do not disassemble or reassemble the charger.

#### 7 Charging  Times

Battery  Type               Battery Capacity                 Charging Times (Appr.)

8 Mechanical Drawing

# 9 Nameplate