1. Install the batteries in the transmitter.
2. Insert the jumper to the Bat port of the receiver.
3. Connect the receiver battery to any one of the channel- ports. Note: at the same time there are two LED’s flashing meaning the receivers are going into bind status.
4. Press and hold the Bind button on the transmitter, and then switch on the transmitter.
5. Observe the LED on the receiver. When the LED stops flashing, the bind was successful. (This process about 10 seconds)
6. Release the Bind button on the transmitter and remove the jumper and receiver battery.
7. Install a servo and receiver battery and then test.
8. If the tests fail, please repeat steps 1-7.
Notes: The negative pin is on the short side of the receiver (i.e. The signal is toward the center of the receiver).